## Slide 1
Takt Time / Lead Time
Lean Manufacturing

## Slide 2
Lean Manufacturing
The Toolbox
Obeyaka / Lean Layout
5S
Small-sized Packaging
Inbound Milkrun
Takt Time
SMED Changeover
Level 1 – Enabler
Standard-
ization
One Piece Flow
2-Box Principle
Mizusumashi / Tow Train
Zero Buffer
Visualization
Level 2 – Basics
Lean Training
Operator-Process Flexibility
Andon
Safety / Ergonomics
Supermarket
Pull / Kanban
Level 3 – Experts
Heijunka / Leveling
Yamazumi / Line Balancing
3P /
Design for Manufacturing
Total Productive Maintenance
Mixed Model Line
Jidoka / Hanedashi
Level 4 – Pro-Tools

## Slide 3
Takt Time
In any production environment it is mandatory to follow a strictly defined speed. That speed is driven by the selling speed of the product. Hence the takt time is calculated based on the customer demand – not measured! Takt time is the pace of a production and indicates the target time per part.

## Slide 4
The Drummer
The drummer plays a major role in all rock bands.
He dictates and keeps time. All other musicians follow at that speed. If he gets too fast or slow, or makes mistakes the song collapses and the band stops playing.
Drums are the heartbeat of a song as the takt is for any production.

## Slide 5: Takt Time
Why do you have to respect a calculated takt time?
Less floor space
A takt enables one piece flow having a huge impact on the required floor space
Produce just-in-time
It is mandatory to follow the speed of the customers to prevent waste
Less fixed capital
Products are sold once been produced instead of being stored.
Room for improvements The takt time reveals weak points in the production. Seize this as an opportunity to improve!
Transparency
Takt time indicates productions behind schedule and allows implementing lean principles
Avoid overproduction
When following the customers demand, no overproduction occurs

## Slide 6: Takt Time
Calculation
  Takt time is calculated based on a time span and the quantity of parts which have to be produced during that time
  The available working time is the time the operators or machine works. Make sure to deduct all kind of downtime (like breaks, machine set-up, cleaning)
  The available working time often is the time per shift deducted by those downtimes (8 hours)
  The result is the takt time. In the shown example the takt time is 19 s. Each 19 seconds a part has to be produced
  The takt time is the overall target for your production
How do you calculate the correct takt time?
1
Define required quantity based on demand
2
Define available net working time
3
Calculate the takt time
4
Align all processes to meet the takt time

## Slide 8
Takt Time / Lead Time
Enabler for…
Obeyaka / Lean Layout
5S
Small-sized Packaging
Inbound Milkrun
Takt Time
SMED Changeover
Level 1 – Enabler
Standard-
ization
One Piece Flow
2-Box Principle
Mizusumashi / Tow Train
Zero Buffer
Visualization
Level 2 – Basics
Lean Training
Operator-Process Flexibility
Andon
Safety / Ergonomics
Supermarket
Pull / Kanban
Level 3 – Experts
Heijunka / Leveling
Yamazumi / Line Balancing
3P /
Design for Manufacturing
Total Productive Maintenance
Mixed Model Line
Jidoka / Hanedashi
Level 4 – Pro-Tools